Sec. 106-240. - Fin fish.

(a)  Intent. It is the intent of this article to provide all residents of the county benefit from the orderly and responsible growth of the aquaculture industry, and particularly, the confined raising of fin-fish species.

(b)  Definitions. For the purpose of this section, the following words, terms and phrases shall have the meanings ascribed to them in this section, except where the context clearly indicates a different meaning:

Adjacent properties means adjacent properties shall be defined as those properties which are either (a) contiguous or (b) separated only by a street or road.

Confined fin-fish operation means an agricultural operation using recirculating aquaculture system within a structure for the production of fin-fish of any species grown for commercial purposes. When applicable this definition also includes associated fully-contained waste storage sites, and/or composters.

Existing dwelling or business means a structure, designed for residential or commercial use which is completed or in the process of being completed on the date a complete application for a confined fin-fish operation permit is received by the zoning administrator.

Processing, waste storage, and related activities means those uses, activities, and structures that may be part of a confined fin-fish operation, which are accessory components of a confined fin-fish operation, including fully-contained waste storage sites, outdoor storage, settling ponds, and composters. Other similar uses require a conditional use permit.

Recirculating aquaculture system means any system used for the rearing of fin-fish where 90 percent or more of system water is recycled on a daily basis.

(c)  Zoning permit required. Zoning approval shall be obtained from the zoning administrator for all proposed fin-fish operations before any construction begins. To obtain a zoning permit, the owner or agent for the owner shall submit a site plan in accordance with section 106-226, drawn to scale and in sufficient detail to show that the proposed confined fin-fish operation meets all applicable requirements of this section, to the zoning administrator for approval. The site plan shall show the size of the parcel, the location and size of existing and proposed buildings and structures on the parcel, the location of proposed entrances and access roads, the location of adjacent zoning district or incorporated town boundaries, and the location of any streams, ditches, or other water bodies on or adjacent to the property. The site plan shall also include a written statement by which the applicant certifies to the zoning administrator that the confined fin-fish operation shown on the site plan meets all applicable setback requirements of this article and that the site plan is a complete and accurate depiction of the confined fin-fish operation as it is to be located on the parcel. The submittal shall also include any applicable applications made to or permits issued from the Department of Environmental Quality.

Zoning permits for confined fin-fish operations shall expire one year after the date of issuance unless substantial construction of the approved facilities has actually commenced, and is progressing toward completion in accordance with the approved site plan.

(d)  Posting of permit. A copy of the zoning permit for approved confined fin-fish operations shall be posted at the entrance to the property in a location that is clearly visible from the roadway.

(e)  Setback verification. The permittee shall contact the county prior to beginning construction on a confined fin-fish operation to arrange for an on-site verification of the required minimum setbacks specified within this article.

(f)  Minimum standards.

(1)  Lot size. The minimum lot size for confined fin-fish operations shall be five acres.

(2)  Setbacks. A recirculating aquaculture system shall be subject to the yard regulations set forth in section 106-58 (agriculture). The minimum setbacks shall apply to a confined fin-fish operation where processing, waste storage and related activities (as defined by this section) occur:

a.  Three hundred feet from any existing dwelling on any adjacent property.

b.  Three hundred feet from any existing business on any adjacent property.

c.  Two hundred feet from any property line(s).

d.  Five hundred feet from incorporated towns or residential zoning district boundaries, subdivisions of ten or more lots, and mobile home parks or travel trailer parks with ten or more units.

e.  Building and structure heights shall be in conformance with section 106-59 (agriculture).

(g)  Zoning districts. Confined fin-fish operations producing less than 1,000,000 pounds per year of whole fish or the processing of less than 500,000 pounds of whole fish per year are allowed by right in the agricultural zoning district or as otherwise permitted by the zoning ordinance. Confined fin-fish operations producing 1,000,000 pounds or more per year of whole fish or the processing of 500,000 pounds or more of whole fish per year will require a conditional use permit in the agricultural zoning district or as otherwise permitted by the zoning ordinance.

(h)  Environment. Confined fin-fish operations shall be conducted in accord with current best management practices without the use of unapproved pharmaceuticals, preventative antibiotics administered in the absence of infection, or growth hormones. The county recognizes Best Management Practices for Flow-Through, Net-Pen, Recirculating and Pond Aquaculture Systems and the American Fisheries Society Fish Culture Section's Guide to Using Drugs, Biologics and Other Chemicals in Aquaculture, February 2011, or as amended.

(Ord. of 11-14-2012)