## Slide 1: Understanding Spatial/Temporal Variability to Improve Confidence in Water Quality Based Establishment Risk

## Slide 2: Lentic Lotic
Lakes/Reservoirs Streams/Rivers
Today’s focus Ask me later

## Slide 3: Mussel Invasion Risk
Introduction Risk
  How likely are mussels to be introduced
Establishment Risk
  How likely are mussels to develop a self sustaining population if introduced

## Slide 4: Establishment Risk
Extent of drawdown
Floating structure presence
Veliger concentration potential
  Enclosed bays, marinas, wave breaks
Residence time
Water quality
  DO
  Temperature
  Calcium
  pH
Other/Unknown

## Slide 5: Establishment Risk
Extent of drawdown
  Floating structures
Veliger concentration potential
Residence time
Water quality
  DO
  Temperature
  Calcium
  pH

## Slide 6
Calcium mg/L
Calcium Establishment Risk Categories
High Risk >20
Low Risk 0-8
Medium Risk 8-20

## Slide 7
pH Risk Categories
High Risk
Low Risk
Low Risk
Medium Risk
Medium Risk
pH Establishment Risk Categories
pH

## Slide 8: Risk Category Development
Lab studies with stable calcium and pH levels
Field studies with natural variability in calcium and pH
  Uncertainty exists in spatial and temporal variability in sampling for field studies
  Acknowledge variability and use mean value
Mean values are often being used for risk analysis

## Slide 9: Variability… Mean vs. Range vs. break points?
Calcium
pH

## Slide 10
All C-PN Reclamation Lentic Site Calcium

## Slide 11
pH is more complicated
All C-PN Reclamation Lentic Site pH

## Slide 12: Biological Activity and pH
Atmospheric CO2 is dissolved into the water
Adding more CO2 (respiration) decreases pH by creating carbonic acid
Taking out CO2 (photosynthesis) increases pH
Carbon dioxide dissolved in water creates CARBONIC ACID

## Slide 13: Photosynthesis
Increases pH
  Mainly above thermocline

## Slide 14: Respiration
Decreases pH
  Mainly below thermocline

## Slide 15: pH Depth Profile
7.61 mean

## Slide 16
Seasonal Variation
7.17 mean

## Slide 22
7.65 mean 2008
7.39 mean all years

## Slide 23
pH is more complicated
All C-PN Reclamation Lentic Site pH

## Slide 24
Interannual variation

## Slide 26
Mean of
Means
Lower 7.3
SE Arm 7.3
Main 7.0
Narrows 7.0
Upper 7.2
Max of Means
8.6
8.4
7.0
7.5
8.2
Min of Means
6.5
6.6
7.0
6.6
6.5
Count of Means
49
43
1
22
42

## Slide 27
Deadwood Overall Variability

## Slide 28: Calcium Data Distribution (982 sites)

## Slide 29: pH Data Distribution (1996 sites)

## Slide 30: Variable pH in the field
Field based pH data for 7.3 cut off is from one study using mean pH at “278” European lakes from other literature

## Slide 31: Constant pH in the Lab
Lab studies at a constant pH show increased mortality with pH <7.3

## Slide 32: Correlation but not Causation?
Lab and field studies show pH of 7.3 as significant
Field sites with a mean of 7.3 will have some areas constantly with higher pH levels where mussels would survive in the lab

## Slide 33: Calcium, pH and Alkalinity Interactions
Calcium and alkalinity are often highly correlated
  Both derived from calcium carbonate
Alkalinity (resistance to acidification) regulates the extent of pH variability
For mean pH of any individual profile to be “low” alkalinity must be also be “low”
“Low” pH= “low” alkalinity = “low” calcium
“Low” pH = “low” calcium

## Slide 34: What is “low?”

## Slide 36
All Columbia basin WQP Lake/Reservoir Data
Notes: In other words, if we can better understand the sites in the red box, we may be able to use the relationship in the green box. So what sites are in the red box?

## Slide 37
15 lake sites on Mount Saint Helens
4 more in volcanic craters in Oregon
5 Mine Sites
2 bogs
4 High Mountain Lakes in Teton NP (70s-81 and n=1)
10 Sites with low pH sample size (n≤3)
2 “Normal” sites all with pH>7.27 Ca<8.5
All WQP Lake/Reservoir Data
Notes: Of the 42 sites with pH<7.3 AND Ca<8…
19 are influenced by volcanic activity
5 are in tailings or during mining disasters
2 are bogs
14 have 3 or fewer sampling events. Most of these events are single sample sand not profiles. At 8 of those 14 sites, data from another site on the same waterbody is available the profile shows a mean pH>7.3
I called out the 4 sites in Teton NP high mountain lakes as they are really old data too
Only 2 of the 42 sites would be someplace I would consider “Normal” and they are very close to not making the cut off for both pH and Ca

## Slide 38: pH Risk: Direct vs Indirect
There are some direct influences of pH on mussels ability to build and maintain shells.
The overall correlation between calcium and pH is only 0.33, but it looks like there is an important relationship with some caveats
Field studies in the literature may describe a relationship between pH and mussels that could be, at least in part indirect through calcium
Notes: So what does this mean? I assume Ramcharan 1992 checked for a correlation between Ca and pH before publishing separate tables and results for each variable in relation to mussel populations. The overall correlation for Reclamation data (0.22) and all WQP Lentic data (0.33) suggest they would not have found any. That doesn’t mean there isn’t a relationship.

## Slide 39: Confidence in calcium risk
Field and lab studies show similar critical values
Field data is not as variable as pH
Low calcium concentrations are more stable as they are below carrying capacity in most if not all of the pH range
Higher calcium concentrations are less stable as fluctuating pH alters the carrying capacity
  Causes of variability are mostly influential above risk break points

## Slide 40
All C-PN Reclamation Lentic Site Calcium

## Slide 41: This pattern is similar for CRB as a whole
695 sites with more than one calcium measurement on the Water Quality Portal
A few exceptions
  Mine sites
  Lakes on volcanoes
  Lakes near ID/NV border
  Lake McDonald
  Flathead Lake

## Slide 42: Confidence in Calcium Risk
With very few exceptions no sites in CRB have calcium measurements in both the low and high risk categories
  Mine sites
  Lakes on volcanoes
  Lakes on ID/NV border (extreme evaporation reduces carrying capacity through salts)
  Lake McDonald (likely data error 14,000 mg/L vs 13mg/L)
  Flathead Lake (Low calcium data is from ’79, Any Ideas? Flooding?)

## Slide 43: Calcium Summary
Calcium seems to be the best metric to inform risk
  Note exceptions for
    Extreme Evaporation
    Local Mining Influence
    Volcanic influence
  If pH is also available, it may not add anything

## Slide 44: pH Summary
If only pH data is available, use with caution
  Surface measurement vs profile
  High spatial and temporal variability
  Unknowns exist where high calcium levels persist at low pH
    Mine influence
    Volcano Influence
“Low” pH could prioritize where to focus calcium sampling

## Slide 45: Small part of overall risk
Introduction Risk
Extent of drawdown
Floating structure presence
Veliger concentration potential
  Enclosed bays, marinas, wave breaks
Residence time
Water quality
  DO
  Temperature
  Calcium
  pH
Other/Unknown

## Slide 46: Potential Future Research
Look at available data to investigate if a single profile with a mean pH less than 7.3 or 7.0 is related to mussel presence and/or calcium levels
Investigate quantifying other risk factors
  Presence of floating marinas
  Veliger concentration potential

## Slide 47
Anthony Prisciandaro
Aprisciandaro@usbr.gov
208-383-2233
Questions?

## Slide 48: Flathead Lake Sites 1979